SECTION 01 41 00

THE AIR BARRIER SYSTEM

PART 1 - 	GENERAL

1.1	SECTION INCLUDES

A.	This section includes administrative and procedural requirements for accomplishing an airtight building enclosure that controls infiltration or exfiltration of air.

1.	The airtight components of the building enclosure and the joints, junctures and transitions between materials, products, and assemblies forming the air-tightness of the building enclosure are called “the air barrier system”.   Services include coordination between the trades, the proper scheduling and sequencing of the work, preconstruction meetings, inspections, tests, and related actions, including reports performed by Contractor, by independent agencies, and by governing authorities.  They do not include contract enforcement activities performed by Architect.

2.	The Contractor shall ensure that the intent of constructing the building enclosure with a continuous air barrier system to control air leakage into, or out of the conditioned space is achieved.  The air barrier system shall have the following characteristics:

a.	It must be continuous, with all joints sealed.

b.	It must be structurally supported to withstand positive and negative air pressures applied to the building enclosure.

c.	Connection shall be made between:

1)	Foundation and walls.

2)	Walls and windows or doors.

3)	Different wall systems.

4)	Wall and roof.

5)	Wall and roof over unconditioned space.

6)	Walls, floor and roof across construction, control and expansion joints.

7)	Walls, floors and roof to utility, pipe and duct penetrations.

3.	Air Barrier Penetrations:  All penetrations of the air barrier and paths of air infiltration / exfiltration shall be sealed.

B.	Inspection and testing services are required to verify compliance with requirements specified or indicated.  These services do not relieve Contractor of responsibility for compliance with Contract Document requirements.

RETAIN PARA BELOW TO CLARIFY THE APPLICABILITY OF PROVISIONS IN THIS SECTION.  MODIFY TO SUIT PROJECT.  COORDINATE MODIFICATIONS WITH GENERAL CONDITIONS AND OTHER DIVISION 1 SECTIONS.  SEE AIA DOCUMENT A201, PARAS 3.3.3, 13.5.1, and 13.5.2.

C.	Requirements of this section relate to the coordination between subcontractors required to provide an airtight building enclosure, customized fabrication and installation procedures, not production of standard products.

1.	Continuity of the air barrier materials and products with joints to provide assemblies.  Continuity of all the enclosure assemblies with joints and transition materials to provide a whole building air barrier system.

2.	Specific quality-control requirements for individual construction activities are specified in the sections of the specifications.  Requirements in those sections may also cover production of standard products.  It is the Contractor’s responsibility to ensure that each subcontractor is adequately and satisfactorily performing the quality assurance documentation, tests and procedures required by each section.

3.	Specified inspections, tests, and related actions do not limit Contractor's quality-control procedures that facilitate compliance with Contract Document requirements.

4.	Requirements for Contractor to provide an airtight building enclosure is not limited by quality-control services required by Architect, Owner, or authorities having jurisdiction and are not limited by provisions of this section.

1.2	RELATED SECTIONS

A.	Division 1 Section Quality Control

B.	Division 1 Section Schedule

C.	Division 1 Section Meetings

D.	Division 3 Section Concrete

E.	Division 3 Section Precast Concrete

F.	Division 5 Section Light Gauge Metal Framing

G.	Division 6 Section Wood Sheathing

H.	Division 7 Section Roofing

I.	Division 7 Section Air Barrier

J.	Division 7 Section Sealants

K.	Division 8 Section Windows

L.	Division 8 Section Exterior Doors

M.	Division 8 Section Curtain Walls

N.	Division 8 Section Revolving Doors

O.	Division 8 Section Skylights

P.	Division 8 Section Storefronts and Entrances.

Q.	Division 8 Section Loading Dock Rollup-up Doors

1.3	RESPONSIBILITIES

RETAIN PARA BELOW FOR NORMAL PROJECTS WHERE CONTRACTOR IS RESPONSIBLE FOR PROVIDING QUALITY-CONTROL SERVICES.  REVISE FOR MULTIPLE PRIME CONTRACTS.  SEE EVALUATIONS FOR FURTHER DISCUSSION.

A.	Contractor Responsibilities:  Unless otherwise indicated as the responsibility of another identified entity, Contractor shall provide coordination of the trades, and the sequence of construction to ensure continuity of the air barrier system joints, junctures and transitions between materials and assemblies of materials and products, from substructure to walls to roof.   Provide quality assurance procedures, testing and verification as specified herein.  Facilitate inspections, tests, and other quality-control services specified elsewhere in the Contract Documents and required by authorities having jurisdiction or by the Owner.  Costs for these services are included in the Contract Sum.

RETAIN SUBPARA BELOW WHEN SOME SECTIONS REQUIRE AN INDEPENDENT TESTING AGENCY TO PERFORM CERTAIN TESTS AND INSPECTIONS.

1.	Organize preconstruction meetings between the trades involved in the whole building’s air barrier system to discuss where each trade begins and ends and the responsibility and sequence of installation of all the air-tight joints, junctures, and transitions between materials, products and assemblies of products specified in the different sections, to be installed by the different trades.

2.	Build a mock-up before proceeding with the work, satisfactory to the Architect, of each air-tight joint type, juncture, and transition between products, materials and assemblies.

RETAIN SUBPARA BELOW WHEN SOME SECTIONS DESIGNATE THE OWNER AS RESPONSIBLE FOR CERTAIN TESTS AND INSPECTIONS.

B.	Associated Services:  Cooperate with agencies performing required inspections, tests, and similar services, and provide reasonable auxiliary services as requested.  Notify the agency sufficiently in advance of operations to permit assignment of personnel.  Auxiliary services required include, but are not limited to, the following:

1.	Provide access to the Work.

2.	Furnish incidental labor and facilities necessary to facilitate inspections and tests.

3.	Take adequate quantities of representative samples of materials that require testing or assist the agency in taking samples.

4.	Deliver samples to testing laboratories.

5.	Provide security and protection of samples and test equipment at the Project Site.

RETAIN THE FOLLOWING PARA ON DUTIES OF THE TESTING AGENCY WHEN CONTRACTOR EMPLOYS THE AGENCY.

C.	Duties of the Testing and Inspection Agency:  The independent agency engaged to perform inspections, sampling, and testing of air barrier materials, components and assemblies specified in individual Sections shall cooperate with the Architect and the Contractor in performance of the agency's duties.  The testing agency shall provide qualified personnel to perform required inspections and tests.

1.	The agency shall notify the Architect and the Contractor promptly of irregularities or deficiencies observed in the Work during performance of its services.

2.	The agency is not authorized to release, revoke, alter, or enlarge requirements of the Contract Documents or approve or accept any portion of the Work.

3.	The agency shall not perform any duties of the Contractor.

IN THE CASE OF MULTIPLE PRIME CONTRACTS, COORDINATE REQUIREMENTS WITH PROVISIONS IN DIVISION 1 SECTION "COORDINATION - MULTIPLE PRIME CONTRACTS." CONSIDER ASSIGNING RESPONSIBILITY FOR COORDINATION TO CONTRACTOR FOR GENERAL CONSTRUCTION.  SEE EVALUATIONS FOR FURTHER DISCUSSION.

D.	Coordination:  Coordinate the sequence of activities to accommodate required services with a minimum of delay.  Coordinate activities to avoid the necessity of removing and replacing construction to accommodate inspections and tests.

1.	The Contractor is responsible for scheduling times for inspections, tests, taking samples, and similar activities.

1.4	PERFORMANCE REQUIREMENTS

A.	Compliance Alternatives:

Pick one or more of the requirements below.

a.	Materials: materials used for the air barrier system in the opaque envelope shall have an air permeance not to exceed 0.004 cfm/ft2 under a pressure differential of 0.3 in. water (1.57psf) (0.02 L/s.m2 @ 75 Pa) when tested in accordance with ASTM E 2178.  Or,

b.	Assemblies of materials and components: shall have an air permeance not to exceed 0.04 cfm/ft2 under a pressure differential of 0.3 in. water (1.57psf) (0.2 L/s.m2 @ 75 Pa) when tested in accordance with ASTM E 2357.  Or:

c.	The entire building: The air leakage of the entire building shall not exceed 0.4 cfm/ft2 under a pressure differential of 0.3 in. water (1.57psf) (2.0 L/s.m2 @ 75 Pa) when tested according to ASTM E 779.

1.5	SUBMITTALS

RETAIN PARA BELOW.  REVISE TO SUIT PROJECT.  IN THE CASE OF MULTIPLE PRIME CONTRACTS, CONSIDER ASSIGNING RESPONSIBILITY FOR COORDINATION OF SUBMITTALS TO CONTRACTOR FOR GENERAL CONSTRUCTION.  SEE EVALUATIONS FOR FURTHER DISCUSSION.

A.	Unless the Contractor is responsible for this service, the independent testing agency shall submit a certified written report, in duplicate, of each inspection, test, or similar service to the Architect.  If the Contractor is responsible for the service, submit a certified written report, in duplicate, of each inspection, test, or similar service through the Contractor.

1.	Submit additional copies of each written report directly to the governing authority, when the authority so directs.

REVISE OR EXPAND SUBPARA BELOW AS REQUIRED TO SUIT PROJECT.

2.	Report Data:  Written reports of each inspection, test, or similar service include, but are not limited to, the following:

a.	Date of issue.

b.	Project title and number.

c.	Name, address, and telephone number of testing agency.

d.	Dates and locations of samples and tests or inspections.

e.	Names of individuals making the inspection or test.

f.	Designation of the Work and test method.

g.	Identification of product and Specification Section.

h.	Complete inspection or test data.

i.	Test results and an interpretation of test results.

j.	Ambient conditions at the time of sample taking and testing.

k.	Comments or professional opinion on whether inspected or tested Work complies with Contract Document requirements.

l.	Name and signature of laboratory inspector.

m.	Recommendations on retesting.

1.6	QUALITY ASSURANCE

RETAIN PARA BELOW.  SPECIFY EXCEPTIONS, SUCH AS ASTM LABORATORY PREQUALIFICATION STANDARDS, IN INDIVIDUAL SECTIONS.  POSSIBLY INSERT REQUIREMENT FOR SUBMITTAL OF PROOF OF QUALIFICATIONS IN THE FORM OF A RECENT REPORT ON THE INSPECTION OF THE LABORATORY BY A RECOGNIZED AUTHORITY.

A.	Qualifications for Air Barrier Testing and Inspection Agencies:  Engage air Barrier inspection and testing service agencies, including independent testing laboratories, that are prequalified and that specialize in the types of air barrier system inspections and tests to be performed.

PART 2 - 	PRODUCTS

(not used)

IF OWNER IDENTIFIES SPECIFIC TESTING AGENCIES TO PERFORM DESIGNATED TESTS AND INSPECTIONS, DELETE "(NOT USED)" ABOVE AND INSERT PARAS IDENTIFYING THE INDEPENDENT AGENCIES HERE.

PART 3 - 	EXECUTION

3.1	REPAIR AND PROTECTION

A.	Upon completion of inspection, testing, sample taking and similar services, repair damaged construction and restore substrates and finishes.  Comply with Contract Document requirements for Division 1 Section "Cutting and Patching."

IN THE CASE OF MULTIPLE PRIME CONTRACTS, CONSIDER ASSIGNING RESPONSIBILITY FOR PROTECTION TO CONTRACTOR FOR GENERAL CONSTRUCTION.  SEE EVALUATIONS FOR FURTHER DISCUSSION.

B.	Protect construction exposed by or for quality-control service activities, and protect repaired construction.

C.	Repair and protection is Contractor's responsibility, regardless of the assignment of responsibility for inspection, testing, or similar services.

3.2	TESTING AND INSPECTION

THE OWNER SHOULD HIRE A COMPETENT THIRD PARTY TESTING AND INSPECTION AGENCY TO PERFORM QUALITY ASSURANCE ON THE AIR BARRIER SYSTEM.  THE SCOPE OF SERVICES SHOULD BE SELECTED AND EDITED FROM THE LIST BELOW BASED ON APPLICABILITY AND IMPORTANCE OF THE PROJECT.

A.	The Owner will hire a testing and inspection agency to provide [Continuous] [Occasional] observation and inspection during installation of the air barrier system.  The testing and inspection agency will provide the following listed services:

1.	Qualitative Testing and Inspection:

a.	Daily reports of observations, with copies to the Owner, Contractor and Architect.

b.	Continuity of the air barrier system throughout the building enclosure with no gaps, holes.

c.	Structural support of the air barrier system to withstand design air pressures.

d.	Masonry and concrete surfaces are smooth, clean and free of cavities, protrusions and mortar droppings.

e.	Site conditions for application temperature and dryness of substrates.

f.	Maximum length of exposure time of materials to ultra-violet deterioration.

g.	Surfaces are properly primed.

h.	Laps in material are 2”minimum, shingled in the correct direction (or mastic applied on exposed edges), with no fish-mouths.

i.	Mastic applied on cut edges.

j.	Roller has been used to enhance adhesion.

k.	Measure application thickness of liquid-applied materials to manufacturer’s specifications for the specific substrate.

l.	Materials used for compatibility.

m.	Transitions at changes in direction, and structural support at gaps.

n.	Connections between assemblies (membrane and sealants) for cleaning, preparation and priming of surfaces, structural support, integrity and continuity of seal.

o.	All penetrations sealed.

p.	ASTM E 1186 “Standard Practices for Air Leakage Site Detection in Building Envelopes and Air Retarder Systems.”

1)	Infrared scanning with pressurization/depressurization.

2)	Smoke pencil with pressurization/depressurization.

3)	Pressurization/depressurization with use of anemometer

4)	Generated sound with sound detection

5)	Tracer gas measurement of decay rate

6)	Chamber pressurization/depressurization in conjunction with smoke tracers

7)	Chamber depressurization using detection liquids

2.	Quantitative tests:

a.	Provide written test reports of all tests performed, with copies to the Owner, Contractor and Architect.

b.	Material compliance for maximum air permeance, ASTM E 2178.

c.	ASTM E 283, Determining rate of Air Leakage Through Exterior Windows, Curtain Walls, and Doors under Specified Pressure Differences Across the Specimen.

d.	Assemblies, ASTM E 2357, test pressure and allowable air leakage rate to be determined by design professional for interior design conditions and location of project.

e.	CAN/CGSB 1986 Standard 149.10, Determination of the Airtightness of Building Envelopes by the Fan Depressurization Method.

f.	CAN/CGSB 1996 Standard 149.15 Determination of the Overall Envelope Airtightness of Office Buildings by the Fan Depressurization Method Using the Building’s Air Handling System.

g.	Whole building, floors, or suites, ASTM E779, Determining Airtightness of Buildings Air Leakage Rate by Single Zone Air Pressurization.

h.	Windows and connections to adjacent opaque assemblies, ASTM E783 method B

i.	Tracer gas testing, ASTM E741

j.	Pressure test, ASTM E330

k.	Bond to substrate, ASTM D4541

END OF SECTION